Kyber modules design progress
Kyber modules design progress
By Pakin Panawattanakul
19/01/2026

---
Presentation Outline
Presentation Outline
Review previous NTT module design	pg. 3
Update New Modules	pg. 4
Result & Verification	pg. 14
Problems	pg. 17
Future work	pg. 19

---
Previous NTT module design
2 Muxes per Cooley Tukey
1 Mux per address in buffer
128 Cooley Tukey = 256 Muxes
256 Address = 256 Mux
512 Muxes

---
Modules
- Montgomery reduce
- fqmul
- Cooley tukey
- NTT
Modules

---
Montgomery Reduce

---
Montgomery reduce
Montgomery reduce
C
System Verilog

---
fqmul

---
fqmul
fqmul
C
System Verilog

---
cooley_tookey
cooley_tookey
no direct C implementation for cooley tookey function
Imitate what each NTT loop do
System Verilog

---
NTT
New Design
NTT
- Using 8 cooley tukey units
- 2 buffers
- Finite state machine
Top module for converting polynomial ring into NTT form

---
NTT description

---
Finite state machine
Finite state machine
No.	Name	Description
0	load	Initial state : load input to buffer_in, set initial variable / Go to compute(1)
1	compute	Compute CooleyTookey until next block is detected / Go to next_blk(2)
2	next_blk	Set variable for next block / If the current stage complete => go to sync_in_out(3) / else => go back to compute(1)
3	sync_in_out	Save data from output buffer to input buffer / go to next_stage(4)
4	next_stage	Set variable for next stage / If (this is the last stage) : go to done(5) / Else : go back to compute(1)
5	done	Save value from output buffer to output, go to idle(6)
6	idle	Do nothing waiting for next enable signal

---
Finite state machine (2)
Finite state machine
0 : Load
2 : Next Block
1 : Compute
Finish stage == no
Last stage == no
Finish stage == yes
4 : Next stage
3 : sync_in_out
Last stage == yes
5 : Done
6 : Idle

---
Verifications
Result & Verifications
- Save RTL output to files
- C test code compare output from RTL to C-reference output
Modules other than NTT are verified by testbench but we will skipped in this presentation

---
NTT Testbench
- Load input from file
- Enable & reset signal
- Write the result to file

---
C testcode
- Read RTL output file
- Mod output with 3329
- Compare with output from C code

---
Problems
- Correct behavioral simulation output but ...
- Resource utilzation is extremely high
  - Main Problem : LUT
  - I/O : Not a real problem

---
Data flow design
Abnomally large cooley_tukey block
I/O are very big : My guess is : not a problem since the real implementation will be internal BRAM or wire or reg, not I/O port

---
Future work
- Deisign other module in encapsulations (Main focus)
- Improve NTT module : reduce resources usage
- Goal : Finish all encapsualtion modules before end of
  Jan 2026